## Slide 1
ECE 5397/6397:
Introduction to Robotics
Lecture 3:
Coordinate transformations, composition of rotations, homogeneous transformations
Reference: Chapter 2.3, 2.4, 2.7 in RD&C
Instructor: Aaron Becker

## Slide 2: Upcoming:
Office hours 2-3:30pm Tues & Thurs, in N386
TA: 2-3:30pm, Mon & Wed in N386
ROS install night: Tues, Jan 26, 7pm, N386
Swarmathon video: http://nasaswarmathon.com/webinars/
This webinar covered: how the Swarmie software works, a close up view of the hardware, the new schedule, how teams will be scored, cash prizes, and exciting opportunities available to you beyond the competition.
If you have already created a Swarmathon webinar account, you can view this recording by entering your Email and Password. If not, all you have to do is to create an account by filling out a short form. Once you have an account, you are then able to participate in all future webinars, as well as watch recordings of past webinars.
Linux/Unix tutorial: Thurs & Fri, Jan 28th, from 10:00am-12:00pm, in the Engineering Computing Center (ECC), Engineering Building 2, Room W129.
HW 1 due Feb 2 at 11:32am
Notes: https://github.com/BCLab-UNM/Swarmathon-ROS for

## Slide 3: Linux tutorials
The ECC/EERC will offer two levels of Linux workshops ­this week - an Introduction to Linux and Intermediate Linux .
The Introduction to Linux Workshop* will be offered on Thurs, Jan. 28th, from 10am-12pm, in the Engineering Computing Center (ECC), Engineering Building 2, Room W129.
Topics covered include:
-Linux/UNIX Systems Overview -Interoperability with Windows
-Linux/UNIX Accounts ­ Email & Personal Web Page
-File Systems, Permissions -System Commands & Applications
The Intermediate Linux Workshop* will be offered on Friday, Jan. 29th, from 10am-12pm, also scheduled in the ECC, Engineering Building 2, Room W129.
Topics covered include:
-Input, Output & Pipes -Compiling UNIX Software Packages
-Symbolic and Hard Links-Setting Environment Variables
-File Transfers & Processes
*If you plan to attend either of the Linux/Unix workshops, you MUST have a UNIX account and be able to login to UNIX before the workshop begins - get your UNIX account at the ECC Front Desk.
All workshops are “hands-on” and free to Engineering students. Seating is limited - no reservations are required.

## Slide 4: Review
Coordinate frame: an origin and 3 mutually-orthogonal, right-hand-rule basis vectors
o0x0y0z0
Rotation matrix is these 3 mutually-orthogonal, right-hand-rule basis vectors:
p1 = Coordinates of p in frame o1x1y1z1
p0 = Coordinates of p in frame o0x0y0z0

## Slide 5: 2.3 Rotational Transforms!
Given a rigid object S with a coordinate frame attached: o1x1y1z1
Given coordinates p1, determine p0
p = ux1+vy1+wz1
Notes: p1 = Coordinates of p in frame o1x1y1z1
p0 = Coordinates of p in frame o0x0y0z0

## Slide 6: p = ux1+vy1+wz1

## Slide 7: Def #1
A rotation matrix R10 can be used to represent the orientation of coordinate frame o1x1y1z1 with respect to o0x0y0z0
Also can transform coordinates of a point from one frame to another
If a given point is expressed relative to
frame o1x1y1z1 by coordinates p1, R10p1 represents the same point expressed relative to the frame o0x0y0z0

## Slide 8: Rotation example

## Slide 9: Example 2.3
Vector v has coordinates
v0=[0,1,1]T, is rotated about y0 by π/2
Notes: Fill in Ry, π/2

## Slide 10: Rotation definitions
A rotation matrix R ∈ SO(3) or R ∈ SO(2), can be represented 3 ways:
A coordinate transformation relating the coordinates of a point p in tw different frames
Orientation of a transformed coordinate frame w.r.t. a fixed coordinate frame
Operator taking a vector and rotating it to give a new vector in same coordinate frame.

## Slide 11: Similarity Transforms
Coordinate frame is defined by set of basis vectors
If A is matrix representation of given linear transformation in o0x0y0z0 and B is the same linear transformation in o1x1y1z1, then A and B are related as

## Slide 12: Draw example 2.4 on board

## Slide 13: Composing Rotations
Write out 2.12 through 2.15 on board

## Slide 14: Composition of Rotations
The frame relative to which the rotation occurs is called the current frame
Frame o0x0y0z0 is the fixed frame
When a rotation R is performed with respect to the world coordinate frame, the current rotation matrix is pre-multiplied by R

## Slide 15: Example 2.8
Then do in-class worksheet

## Slide 16: Homogenous transforms
4 x 4 matrices to represent both rotation and translation. Key for robotics frames.
H =

## Slide 17: Homogenous transforms
we must augment vectors, so p0 becomes P0:
If rigid motion H is relative to the current frame, then post-multiply
If rigid motion H is relative to the fixed frame, then pre-multiply

## Slide 18: For the Next Class
Github checkin: need one per team
Study Sections 2.5 & 2.6 for Lecture 4
  This is important: I want you to come prepared for each class by reading ahead, and have an idea of what to expect
    Write down your questions and bring them with you
    I may do a quiz in class based on your assigned reading
  This is good for you
    Advance reading will help you grasp the subject with much less effort

## Slide 19: In class worksheet