## Slide 1
ECE 5397/6397:
Introduction to Robotics
Welcome & Lecture 1
Reference: Chapter 1, RD&C
Instructor: Aaron Becker
youtube.com/aabecker5/
www.SwarmControl.net

## Slide 2: Welcome!
Fundamentals of robotics: the Mathematical modeling of robots as mechanical devices
Definitions:
  Robot: from Czech word for work “robota”: A robot is a reprogrammable, multifunctional manipulator designed to move material, parts, tools, or specialized device through variable programmed motions for the performance of a variety of tasks
  Robots come from teleoperators + numerically controlled milling machines
ROS install night: Tuesday, Jan 26, 7pm, N386
Notes: Teleoperators from WWII to handle radioactive materials
CNC developed because of high precision required to machine certain items

## Slide 3: “Robot”
Notes:   A robot is a reprogrammable, multifunctional manipulator designed to move material, parts, tools, or specialized devics through variable programmed motions for the performance of a variety of tasks

## Slide 4: Worldwide robots
plot
Notes: http://www.ifr.org/industrial-robots/statistics/

## Slide 5: Important
This course will use a lot of mathematics
  This material can only be learned from solving practice problems every day
  Every class will have an in-class activity
  Come prepared to each class
  Do not fall behind
Immediate Action Items for you:
  Brush up on your Math, especially Trigonometry (really), and Linear Algebra (appendix A and B)
  Sign up for swarmathon & github https://github.com/UH-ECE6397
  Download A Gentle Introduction to ROS

## Slide 6: Software
We will use MATLAB for some of our assignments and examples
You learned to use in ECE 1331
  You have a month to brush up your MATLAB skills
Get latest MATLAB version on your computer
  Free campus-wide license
Each 3-person team needs access to a computer with ROS, and each member needs time on it
Swarmathon uses C++, ROS has wrappers for any language

## Slide 7: Optional Software
I like to use Mathematica for playing around with robots http://demonstrations.wolfram.com/author.html?author=Aaron+Becker
  Fun and informative
  Great for verifying solutions to problems
  You are welcome to try it, but it is not required
Free download for all UH students and faculty
A published, intro-to-robotics-Mathematica demonstration (with Dr. Becker as the last author), will add 2.5 to 6% to your final grade. Some topics include  demonstration on inverse velocity kinematics as robot traces out a square and circle,  calculation and plot of manipulability ellipse of robot arm at different configurations,  demonstration on DH parameters,  visualization of robot workspace  configuration vs. workspace of an RR robot  visualization of workspace singularities.

## Slide 8: Instructor
Instructor: Aaron Becker
  Email (best): atbecker@uh.edu
  Phone: 713-74306671
  Office: Room N338, Engineering Building 1
  Office hours: Tues & Thursdays 2-3:30pm
TA: Li Huang
  Email: : lihuang.mech@gmail.com
  Phone: (713) 743-7296
  Office hours: 2:00-3:30pm, Mon & Wed

## Slide 9: How Grades are Assigned
Item | Schedule | Points | Adjustment
Worksheet (in class) | One per lecture | 10% | Lowest score dropped
Homeworks | One per chapter | 30% | Lowest score dropped
Lab /ROS | distributed | 20% | 
Mid-term 2 (Ch 3 – 4) | April 4th | 20% | 
Final Exam (Ch 1 – 6) | Finals Week (Date TBD) | 20% | 
Relative Grading
  All students are ranked based on overall grade
  Letter grades based on your rank in class
Generous reward for effort
  Attempt everything & do your best
  I’m looking for 1-2 new grad students
Be honest and stay out of trouble
  Simply not worth it!

## Slide 10: Course Policies
This course is about learning fundamental concepts
  Do the problems by hand first, and use calculators/software to verify
  For the exams, calculators/computers/tablets are not allowed
Please read the handout carefully
Ask questions, get answers
Give feedback – help me teach you better

## Slide 11: Required Textbook
We will follow the book closely
  Chapters 1, 2, 3, 4, 5, 11, 12.
  Bring it to each class – we will use it
Helpful handouts will be provided when needed
Recommended Books:
ROS textbook: A Gentle Introduction to ROS. Free at https://cse.sc.edu/~jokane/agitr/. Print version at $12.50 at
Cost: $95

## Slide 12: Assemble your teams by Jan 28
Swarmathon: 3 to 4-person teams. Each team completes 3 challenges in ROS, concluding with in-class competition on Swarmathon challenge.
Robot Arm: 2-person teams.
Toyrus.com
http://marvel-movies.wikia.com/wiki/The_Avengers_(team)
Notes: Pick a diverse team (a programmer, a mechanical person, a math person)

## Slide 13: Two Projects
Swarmathon details: webinar Jan. 22
http://nasaswarmathon.com/
D N328 reserved – you can watch from anywhere
Robot arm: purchase motors and Arduino as soon as you have a team
http://www.instructables.com/id/MeArm-Robot-Arm-Your-Robot-V10/

## Slide 14: Mathematical Modeling of Robots
Robot manipulator is composed of links connected by joints to form a kinematic chain
Revolute joint (hinge), R
Prismatic joint (slide), P

## Slide 15: Symbolic Representation
ith joint connects link i and i+1
zi is axis of rotation of revolute, axis of translation of prismatic
Joint variables θi revolute, di prismatic
What type of Robot is this?
How do we describe the configuration?
RRR
θ1 θ2 θ3

## Slide 16: Configuration Space
Configuration of a manipulator: complete specification of the location of every point on the manipulator
Configuration space: set of all configurations
Denote with vector q = [q1, q1,…, qn]
Degrees of freedom (DOF) number of parameters to minimally specify configuration
Configuration space
q = θ1 θ2
Notes: ----- Meeting Notes (1/19/16 12:51) -----
add q2 aqn

## Slide 17: Configuration Space
An object in space has 6 DOF:
  3 positioning (x,y,z)
  3 orientation (θ,ϕ,ψ)
Manipulator usually has 6 DOF
Manipulator with more than 6 DOF is kinematically redundant
Notes: Get a volunteer: is their arm kinematically redundant
kinematically redundant
Useful for reaching around or behind obstacles

## Slide 18: Tricky: State Space / Workspace
Configuration describes geometry, not dynamics
State of manipulator: set of variables that with description of manipulator dynamics and future inputs, determines the future time response of the manipulator
State space: set of all possible states
For robot manipulator, state is joint variables q and joint velocities
Workspace is total volume swept out by the end effector as manipulator executes all possible motions
Reachable workspace: set of points reachable
Dextrous workspace: set of points where all orientations are possible
Statenspace: [θ1, θ2, d3, d/dtθ1, d/dtθ2, d/dtd3]
workspace
Notes: Workspace often constrained

## Slide 19: Classifying Robot Manipulators
Power: electric/hydraulic/pneumatic
Method of control: servo/nonservo
Application area: assembly/nonassembly
Geometry: RRR, RRP, etc, serial vs. parallel
Fun: http://new.abb.com/products/robotics/robot-selector
Notes: Fun video: http://search-ext.abb.com/library/Download.aspx?DocumentID=9AKK106713A0297&LanguageCode=en&DocumentPartId=&Action=Launch

## Slide 20: Classifying Robot Manipulators
Power: electric/hydraulic/pneumatic
Mitsubishi electric, wisegeek.com, festo.com
Electric: cheaper, cleaner, quieter
Hydraulic: stronger
Pneumatic: often inexpensive/simple, precise control hard (but see Festo)

## Slide 21: Classifying Robot Manipulators
Method of control: servo/nonservo
Nonservo: open-loop
Servo (closed loop)
  Point-to-point: can specify desired position of end-effector
  Continuous path: follows trajectories
Geometry: serial vs parallel
Serial and parallel robots from Mitsubishi
The 4-DOF Quattro robot by Adept Technology.
Notes: Fun video: http://search-ext.abb.com/library/Download.aspx?DocumentID=9AKK106713A0297&LanguageCode=en&DocumentPartId=&Action=Launch

## Slide 22: Robot System
Notes: Manipulator more than just series of mechanical linkages. The mechanical arm is just a component in the robotic system

## Slide 23: Why Rotational Links?
Rotational links have lower resolution, kinematic coupling between links, and harder math.

## Slide 24: Wrists
Sphereical wrist: greatly simplifies kinematic analysis: decouples position and orientation of end effector

## Slide 25: End effector/ Hand

## Slide 26: Common Kinematic Arrangements
Time to Stand up and act them out!
Really – stand up!

## Slide 27: Articulated Manipulator: RRR
Articulated Manipulator, AKA revolute, elbow, anthropomorphic

## Slide 28: Articulated Manipulator: RRR
Articulated Manipulator, AKA revolute, elbow, anthropomorphic

## Slide 29: Spherical Manipulator: RRP
One of the first manipulator designs

## Slide 30: SCARA: RRP
Selective Compliant Articulated Robot for Assembly

## Slide 31: Cylindrical: RPP

## Slide 32: Cartesian: PPP

## Slide 34: Activity: problem 1, handout
Power: electric/hydraulic/pneumatic
Method of control: servo/nonservo
Application area: assembly/nonassembly
Geometry: RRR, RRP, etc., serial vs. parallel
arc welding packing
grinding,
parts inspection,
small parts assembly,
cleaning/spraying,
spot welding,
painting

## Slide 35: Outline Of Class
want manipulator to move from home to A to follow surface contour to B at constant velocity while maintaining force F.
Notes: Typical Application: an industrial manipulator. This one has a metal grinding wheel, job is to remove a certain amount of material from a surface. “What are basic issues? What do we need to learn?”

## Slide 36: Coordinate System Ch. 2
Describe position of tool, A, B in common coordinate system (Ch. 2: coordinate sys. and transformations)
Typically robot has sensors to measure θ1, θ2, Forward Kinematics: determine position and orientation of end effector or tool in terms of joint variables

## Slide 37: Forward Kinematics Ch. 3.2
a1
a2
Notes: Do this on the board

## Slide 38: Forward Kinematics ch 3.2
a1
a2
Location of end effector
Orientation of tool frame found by projecting coordinate frame 2 onto 0:
Rotation matrix:
Orientation of coordinate frame 2 according to coordinate frame 0
Notes: Do this on the board
We will use homogenous coordintes and homogenous transformations to simplify

## Slide 39: Inverse Kinematics Ch 3.3
To command the robot to move to A we need to determine θ1, θ2. [nonlinear equations to invert]
Notes: Elbow up/ elbox down

## Slide 40: Inverse Kinematics Ch 3.3

## Slide 41: Inverse Kinematics Ch 3.3
Law of cosines: triangle sides a,b,c, and angle opposite c is θc,
Rotation matrix

## Slide 42: Velocity Kinematics Ch 4
Differentiate kinematic equations:
J = Matrix Jacobian

## Slide 43: Inv. Velocity Kinematics Ch. 4
Notes: Determinate By addition identity

## Slide 44: Singular Configurations Ch. 4

## Slide 45: Summary
This course is about robot manipulators & ROS
We looked at a basic 2-link system:

## Slide 46: For the Next Class
Work through the textbook examples in Chapter 1
Study Sections 2.1, 2.2 for Lecture 2
  This is important: I want you to come prepared for each class by reading ahead, and have an idea of what to expect
    Write down your questions and bring them with you
    I may do a quiz in class based on your assigned reading
  This is good for you
    Advance reading will help you grasp the subject with much less effort

## Slide 47: In class worksheet
3. Grad students: suppose we could close every factory today and reopen them tomorrow fully automated with robots. What would be some of the economic and social consequences of such a development?
Undergrads: Suppose a law were passed banning all future use of industrial robots. What would be some of the economic and social consequences of such an act?