## Slide 1
ECE 5397/6397:
Introduction to Robotics
Lecture 2:
Rotation matrices, SO(n)
Reference: Chapter 2.1 &2.2 & Appendix B, RD&C
Instructor: Aaron Becker
Also, see: https://en.wikipedia.org/wiki/Rotation_matrix
and http://mathworld.wolfram.com/RotationMatrix.html
Notes: Bring Tinker Toys – show rotation matrices.
Bring a screw-driver

## Slide 2: Welcome!
ROS install night: Tuesday, Jan 26, 7pm, N386
Two simple examples of hobbyists working with robot kinematics and arduinos:
2-dof arm: https://www.youtube.com/watch?v=8DVK206u0zY
6-DOF arm https://www.youtube.com/watch?v=cod_SNq-d6c
Notes: Teleoperators from WWII to handle radioactive materials
CNC developed because of high precision required to machine certain items
----- Meeting Notes (1/21/16 12:04) -----
install night

## Slide 3: Outline Of Class
want manipulator to move from home to A to follow surface contour to B at constant velocity while maintaining force F.
Notes: Typical Application: an industrial manipulator. This one has a metal grinding wheel, job is to remove a certain amount of material from a surface. “What are basic issues? What do we need to learn?”

## Slide 4: Coordinate System Ch. 2
Describe position of tool, A, B in common coordinate system (Ch. 2: coordinate sys. and transformations)
Typically robot has sensors to measure θ1, θ2, Forward Kinematics: determine position and orientation of end effector or tool in terms of joint variables

## Slide 5: Forward Kinematics Ch. 3.2
a1
a2
Notes: Do this on the board

## Slide 6: Forward Kinematics Ch. 3.2
a1
a2
Location of end effector
Orientation of tool frame found by projecting coordinate frame 2 onto 0:
Rotation matrix:
Orientation of coordinate frame 2 according to coordinate frame 0
Notes: Redo the rotation for x1, then x2 on the board
We will use homogenous coordinates and homogenous transformations to simplify

## Slide 7: Inverse Kinematics Ch. 3.3
To command the robot to move to A we need to determine θ1, θ2. [nonlinear equations to invert]
Notes: Elbow up/ elbox down

## Slide 8: Inverse Kinematics Ch. 3.3

## Slide 9: Inverse Kinematics Ch 3.3
Law of cosines: triangle sides a,b,c, and angle opposite c is θc,
Rotation matrix

## Slide 10: Velocity Kinematics Ch 4
Differentiate kinematic equations:
J = Matrix Jacobian

## Slide 11: Inv. Velocity Kinematics Ch. 4
Notes: Determinate By addition identity

## Slide 12: How many solutions to the inverse kinematics problem are there?
4 regimes:
Notes: Inf. Solutions
2 solutions
1 solution
0 solutions

## Slide 13: Singular Configurations Ch. 4

## Slide 14: In class worksheet
Pretend this is a quiz.
You have 15 minutes to accomplish as much as possible.
Then, we will exchange sheets and “grade” it
This will tell you what you need to review.
Notes: 15’ hdmi cord

## Slide 15: Quiz answers (write correct answer)

## Slide 16: Quiz answers (write correct answer)

## Slide 17: Quiz answers (write correct answer)
Notes: ----- Meeting Notes (1/21/16 12:53) -----
alpha is a scalar, x and y are vectos (fix WS

## Slide 18: Representing Positions
Synthetic approach: reasons about geometric entities (points, lines, etc.)
Analytic approach: represent entities with coordinates or equations, reasoning via algebraic manipulation. Requires a coordinate frame:
Notes: Coordinate frame: an origin (single point in space) and two or three orthogonal axes for 2d or 3d space
Synthetic approach: x0 and y0 are orthogonal. Xo cross yo is perpendicular to page.

## Slide 19: Representing Positions
5
6
10
5

## Slide 20: Representing Positions
5
6
-2.8
3.5
10
5
-10.6
4.2

## Slide 21: Vectors = free vectors
5
6
-2.8
3.5
10
5
-10.6
4.2
Notes: On board: points refer to specific locations in space, a vector can be moved to any location

## Slide 22: Rotation in the plane
o1x1y1 obtained by rotating o0x0y0 by θ
Problems:
discontinuity at θ = 2π
What do we do in 3D?
This is a rotation matrix
Notes: Write out R01

## Slide 23: Rotation Matrix
Show this is commutative
Because column vectors are unit length and mutually orthogonal the matrix is orthogonal
A such n x n matrices are called SO(n), Special Orthogonal group of order n
Notes: From page 40

## Slide 24: Properties of SO(n)
such n x n matrices are called SO(n), Special Orthogonal group of order n
Properties
Notes: Page 41

## Slide 25: Rotation in Three Dimensions
A basic rotation matrix
3 properties:
Notes: 2.3
2.4
2.5
Page 42

## Slide 26: 02_04
02_04
Relative Orientation
Notes: 02_04.jpg

## Slide 27: Summary
Reviewed Vectors from Linear Algebra
Representing Positions
Representing Rotations

## Slide 28: For the Next Class
Study Sections 2.3,2.4,2.7 & Appendix B for Lecture 3
  This is important: I want you to come prepared for each class by reading ahead, and have an idea of what to expect
    Write down your questions and bring them with you
    I may do a quiz in class based on your assigned reading
  This is good for you
    Advance reading will help you grasp the subject with much less effort