## Slide 1
ECE 5397/6397:
Introduction to Robotics
Lecture 5:
Forward kinematics: Denavit-Hartenberg convention and the derivation of D-H transformation matrix, assigning link frames using the DH convention.
Reference: Chapter 3.1 and 3.2, RD&C
Instructor: Aaron T. Becker

## Slide 2: Resources
https://www.youtube.com/watch?v=rA9tm0gTln8
http://demonstrations.wolfram.com/ForwardAndInverseKinematicsOfTheSCARARobot/
Notes: How many robots?

## Slide 3: Update!
We’re ordering robot parts today. How many want to make a robot arm (at least 1 arm per team)
We’re scaling back the Swarmathon & ROS component of the class.
  Still have assignment on the turtle simulator
  Still need to have one person in the team who can run the simulation code (or have time to use UH computer with ROS)
The course gets easier after inverse kinematics
HW 2 on Fwd. Kinematics due Feb 11
Notes: How many robots?

## Slide 4: Overview
https://www.youtube.com/watch?v=rA9tm0gTln8
How can we assign coordinate frames to this manipulator?
Notes: Draw in the parameters on this

## Slide 5: 03_01
Elbow Manipulator
Notes: 03_01.jpg

## Slide 6: Define
Forward kinematics: determine position and orientation of the end effector given values of joint variables of robot
Inverse kinematics: determine the values for joint variables given the end-effector’s position and orientation
Rule: each joint a single DOF
Ball and socket, 2DOF
Spherical Wrist, 3 DOF
Robot has n joints and n+1 links. Start at link 0
Joint i connects links i-1 to i.
When joint i moves, link i moves
Label base frame as 0, attach coordinate frame to each link.
Base frame is the inertial frame

## Slide 7: Homogenous Transform for each link
A coordinate frame has 6 DoF
Our convention adds two constraints
Notes: Write the DH constraints on the board

## Slide 8: DH Constraints
DH1: The axis x1 is perpendicular to the axis z0
DH2: The axis x1 is intersects the axis z0
Notes: Draw in the parameters on this

## Slide 9: DH Constraints
DH1: The axis x1 is perpendicular to the axis z0
DH2: The axis x1 intersects the axis z0
Notes: Draw in the parameters on this

## Slide 10: Angle Convention
Right-hand rule

## Slide 11: DH procedure

## Slide 12: Two link planar manipulator

## Slide 13: Two link planar manipulator

## Slide 14: Two link planar manipulator

## Slide 15: 3-link planar arm: draw it
Work in pairs

## Slide 16: 3-link planar arm, answer

## Slide 17: Three-link Cylindrical Robot

## Slide 18: Three-link Cylindrical Robot Ai

## Slide 19: Three-link Cylindrical Robot, T

## Slide 20: Two-link Cartesian Robot:

## Slide 21: Two-link Cartesian Robot:

## Slide 22: For the Next Class
Study Ch 3.1 and 3.2
Ch1 & 2 A Gentle Introduction to ROS for Lecture 6